## Slide 2: Classification
Digital Architectures
Delay based PUFs:
  RO-PUF
  TERO-PUF
  Arbiter-PUF
  Glitch PUF
Memory based PUFs:
  SRAM-PUF
  FF-PUF
  L-PUF
Hybrid PUFs:
  Composite PUF
  Double Arbiter PUF
Security types
Weak PUF:
  Small CRP space (or only 1)
  The response(s) should never be revealed.
  Good for private key generation
Strong PUF:
  Large CRP space
  The response(s) could be revealed if this challenge-pair won’t be used again.
  Need the ensure that response can not be predicted.
  Good for authentification.

## Slide 3: Arbiter PUF
Delay based, Strong PUF
Variations: XOR Abriter, Feed-forward Arbiter, Reconfigurable, Interpose

## Slide 4: Ring oscillator PUF
Delay based, Weak PUF
Variations: reconfigurable, transcient-effect, bistable ring PUF

## Slide 5: Anderson PUF (FPGA)
Delay based, Strong PUF

## Slide 6: SRAM PUF / FF PUF
Memory based, Strong PUF

## Slide 7: Butterfly PUF / Latch PUF
Memory based, Strong PUF

## Slide 8: Double arbiter PUF
Hybrid, Strong PUF

## Slide 9: Composit PUF (RO + arbiter)
Hybrid, Strong PUF

## Slide 10: PUF characterization metrics
Reliability:
  Probability of “correct” response => 100%
Uniformity:
  Probability that a bit response is “0” (or “1”) for a given challenge => 50%
Uniqueness (intra and inter):
  Mean distance between different PUF’s CRP => 50%
Bit-aliasing (intra and inter):
  Probability that a bit response is “0” (or “1”) accross different PUF’s responses for a given challenge => 50%.
  Indicator of a biased implementation.

## Slide 11
Abreviation | Name | Architecture | Security type | Uniqueness | Reliability | Uniformity | Bit-Alias | ML robust | Area (slices) | Bit length | Target FPGA
A-PUF | Abriter | Delay | Strong | 41.53% | 95.50% | - | - | Good | 2816 | 64 | Artix-7
 |  |  |  | 18.37% | 99.76% | 55.69% | 19.57% | Weak | - | 128 | Virtex-5
 |  |  |  | 44.30% | 96.00% | 48.45% | - | Weak | 234 | 256 | Spartan-6
FF-XOR-APUF | Feed forward XOR arbiter | Delay | Strong | 49.20% | 89.50% | 50.00% |  | - |  | 64 | Artix-7
LR-PUF | Logically reconfigurable | Delay | Strong | - | - | - | - | Weak | 425 | 64 | Spartan-6
IPUF | Interpose | Delay | Strong | 49.25% | 89.50% | 55.90% | - | - | - | 64 | Artix-7
RO-PUF | Ring Oscillator | Delay | Weak | 49.33% | 95.45% | 49.50% | - | Good | - | 186 | Virtex-5
 |  |  |  | 48.30% | 97.88% | 50.13% | 51.80% | - | 747 | 283 | Spartan-3
 |  |  |  | 47.13% | 99.16% | 50.61% | - | Good | 82 | 256 | Spartan-6
 |  |  |  | 49.83% | 99.35% | - | - | Weak | - | 255 | Artix-7
Loop PUF | Loop | Delay |  | 49.94% | 95.00% | 50.00% | - | Good | - | 15 | Cyclone II
TERO-PUF | Transcient Effect Ring Oscillator | Delay | Weak | 48.00% | 98.30% | - | - | Good | - | 126 | Cyclone II
 |  |  |  | 48.50% | 85.00% | - | - | Good | - | 128 | Spartan-6
BR-PUF | Bistable Ring | Delay | Strong | 40.67% | 98.22% | - | - | Weak | - | 64 | Spartan-6
Anderson-PUF | Anderson | Delay |  | 47.65% | 96.40% | - | - | Good | - | 128 | Virtex-5
 |  |  |  | 46.25% | 97.63% | 45.88% | 45.88% | Good | - | 128 | Zynq-7000
Glitch-PUF | Glitch | Delay |  |  |  |  |  |  |  |  | 
SRAM-PUF | Static random-acces memory | Memory | Strong | 49.97% | 88.00% | - | - | Good | - | 128 | -
FF-PUF | Flip-Flop | Memory | Strong | 50% (pos prod) | 95.00% | - | - | Good | - | 128 | Virtex II
Butterfly-PUF | Butterfly | Memory |  | 43.16% | 96.20% | - | - | Good | 130 | 50 | Virtex-5
ID-PUF | identfication | Memory | Weak | 45.60% | 99.42% | - | - | Good | 128 | 128 | Spartan-6
L-PUF | Latch | Memory |  | 49.32% | 98.80% | 44.65% | 44.65% | Good | 128 | 127 | Spartan-3
 |  |  |  | 49.00% | 96.34% | - | - | Good | 256 | 256 | Spartan-6
 |  |  |  | 49.24% | 98.87% | - | - | Good | 324 | 256 | Spartan-6
 |  |  |  | 48.10% | 99.19% | 50.20% | - | Good | 54 | 256 | Spartan-6

## Slide 12: Improve reliability
Calibration
  For design like RO-PUF that compare different elements, we can use only the combination where the different is large enough. Trade off with numbre of CRP available.
ECC
  Bit correction of the response.

## Slide 13: Improve Bit-aliasing
Issu:
  Delay bias in the LUT6 of the Artix-7
Solution:
  Ensure same number of path D(0) and D(1). Tradeoff with CRP size

## Slide 14: Neural networks attacks
Entropy
  Indicate the overall difficulty to predict a response.
Bit-wise entropy
  Indicate which bits are the more vulnerable (gives the most information about the overall response)
Bit-bias
  Indicator of the bias of each bit.
Bit-bias standard deviation
  Potential indicator for fast NN resistance characterization

## Slide 15: Interesting aspect
Hybrid PUF
ECC
PVT
Artix-7LUT6 delay bias mitigation
TERO final state ?